## Slide 1: PFDHA Benchmarking Study Step 1: Model Owner Testing
IAEA PFDHA Benchmarking Group

## Slide 2: Content
Introduction
Objectives and scope of Step 1
Members of the WG and MO
Test Cases
Logic Trees for Cases
Requested Results
Future Actions

## Slide 3: Introduction
In the IAEA Safety Standard SSG-9, PFDHA is recommended to evaluate fault displacement hazard for existing Nuclear Installations in the event that a capable fault is discovered and cannot be avoided.
Given the fact that PFDHA is a relatively new practice, the IAEA Member States wish to have more practical guidance on PFDHA.
In response to this, EESS/IAEA has been leading efforts to prepare IAEA Technical Documents (TecDocs) on two topics: 1) to document the state of practice of PFDHA, including methodologies and case histories, and 2) to document example implementations of PFHDA in a benchmarking study.

## Slide 4: Introduction
We envision the PFDHA benchmarking study as consisting of three steps:
  Step 1 – Validation of current published models and model comparison
  Step 2 – Model implementation for two scenario sites
  Step 3 – Documentation of model validation, comparison, and test case implementation (in an IAEA TecDoc).
Step 1 includes a simple fictional scenario with pre-defined seismic source parameters. Fault displacement model authors are asked to produce results implementing their published models.
The goal of Step 1 is to engage with the owners/originators of the currently published PFDHA models and have them provide reference hazard curves.
The 2nd step will expand to include other teams with experience in implementing PFDHA.

## Slide 5: Objectives and Scope of Step 1
Introduce PFDHA Model owners/originators to IAEA Benchmarking project
Document intended uses/limitations of models as interpreted by originators
Establish “baseline” hazard curves for later validation exercises
Figure out details for Step 2
Holding a meeting (01/20/2021) to discuss outcomes and future actions

## Slide 6: Objectives and Scope of Step 1 continued
IAEA provides:
  Site coordinates and site dimensions (in Excel and shapefile format)
  Source characterization logic trees (parameter values and weights)
Model authors provide:
  Fault displacement equation logic tree (parameter values and weights)
  Results as tables, plots and PowerPoint presentation
  Short answers to questions about approach

## Slide 7: Members of the WG and MO
IAEA PFDHA Benchmarking Working Group (WG):
  Supervisor: Y. Fukushima (IAEA)
  Managing Consultant: A. Valentini (IAEA)
  Advisors: S. Thompson (LCI) – T. Sakai (CRIEPI) – E. Viallet (EDF) – M. Ono (IAEA)
Model Owners working group for Step 1 (MO):
  B. Youngs (for Youngs et al., 2003)
  R. Chen (for Petersen et al., 2011)
  R. Moss (for Moss and Ross, 2011)
  T. Annaka (for Takao et al., 2013-2016)
  F. Visini (for Nurminen et al., 2020)

## Slide 8: Test Cases
List of Test Cases for Step 1: based on Futagawa fault zone (FFZ) characterization by HERP (2015)
Base Case
  Kumamoto Prefectural Office Site: z = 100 m, closest distance site-fault (r = 5.2 km)
  Ruptures are combinations of three FFZ segments (in red)
  Add logic tree branch alternatives to magnitude and mean rate
Sensitivity Cases
  Alternative fault source: SFZ (r = 0.6 km)
  Primary fault displacement hazard (r = 0 km)
    Add Floating* FFZ source alternative (*see slides 18-19)
  Primary hazard, SFZ alternative source
  Increase distance from site to FFZ (r = 10 km)

## Slide 9
HERP map of sources
1
2
3
24 km
22 km
32 km
5.2 km
0.6 km
simplification
Futagawa
Fault Zone
(FFZ)
Suizenji
Fault Zone
(SFZ)
Step 1 model of sources

## Slide 10: Site and sources coordinates for test cases
Uto fault source
Futagawa fault source
r = 10 km site
SFZ site
r = 0 site
Uto Hanto North fault source
Base Case
site
Source geometry parameters:
Uto
  L = 22 km (l/L = 0.23)
Futagawa + Uto
  L = 46 km (l/L = 0.37)
Uto + Uto Hanto North
  L = 54 km (l/L = 0.1)
Futagawa + Uto + Uto Hanto North
  L = 78 km (l/L = 0.37)
All coordinates (lon, lat) are listed in the Excel file and provided in a shapefile

## Slide 11: Base Case – Kumamoto Site
Site coordinates (x1,y1) – off-fault = 130.7417°, 32.7899°
Site dimension (z) = 100 m × 100 m
Closest Distance, FFZ: r = 5.22 km
Map Accuracy = Approximately Located

## Slide 12: Base Case: Distributed fault displacement hazard
3
2
1
2
+
1
2
+
+
FFZ, r = 5.2 km; z = 100 m
5.2 km
5.2 km
5.2 km
M 7.2
(46+32
= 78 km)
M 6.9
(24 + 22
= 46 km)
M 6.5
(22 km)
2
3
+
5.2 km
M 7.0
(22 + 32
= 54 km)

## Slide 13: Base Case Source Logic Tree – single path
Futagawa + Uto (1+2)
Futagawa + Uto +
Uto-Hanto-North (1+2+3)
Fault Source
Magnitude
Mean Rate (×10-5 yr-1)
14
Max Rupture Length
Max Rupture Thickness
Average Dip
6.5
6.9
7.0
Mag PDF
Maximum
Magnitude
18.9
46
14
68.6° NW
Maximum
Magnitude
54
14
60° NW
Maximum
Magnitude
1.28
3.53
22
Uto (2)
60° NW
1.28
7.2
78
14
64.6° NW
Maximum
Magnitude
Uto + Uto-Hanto-North (2+3)

## Slide 14: Base Case Source Logic Tree – multi-path. Model epistemic uncertainty in source mag and rate
Futagawa + Uto (1+2)
Futagawa + Uto +
Uto-Hanto-North (1+2+3)
14
6.5
Maximum
Magnitude
46
14
68.6
Maximum
Magnitude
54
14
60
Maximum
Magnitude
22
Uto (2)
60
78
14
64.6
Maximum
Magnitude
Uto + Uto-Hanto-North (2+3)
Fault Source
Magnitude*
Mean Rate** (×10-5 yr-1)
Max Rupture Length
Max Rupture Thickness
Average Dip
Mag PDF
Notes:
# the complete list of parameters is listed in the excel file
*Magnitude uncertainty reflects a factor of 2 uncertainty in seismic moment per event for each source
**Mean rate uncertainty is a factor of 3 about the middle branch
6.7 [0.2]
6.5 [0.6]
6.3 [0.2]
56.7 [0.2]
18.9 [0.6]
6.3 [0.2]
#

## Slide 15: Sensitivity Cases – Kumamoto Site
Case 1: source is SFZ (not FFZ)
Site coordinates (x1,y1) – off-fault = 130.7417°, 32.7899°
Site dimension (z) = 100 m × 100 m
Closest Distance, SFZ: r = 0.60 km
Map Accuracy = Inferred
Case 2: site is ON FFZ (principal faulting)
Site coordinates (x2,y2) – on-fault = 130.7656°, 32.7474°
Distance r = 0 km
Case 3: site is ON SFZ (principal faulting)
Site coordinate (x3,y3) – on-SFZ = 130.7467°, 32.7936°
Closest Distance r = 0 km
Case 4: site is 10 km from FFZ
Site coordinate (x4,y4) – off-FFZ = 130.7196°, 32.8288°
Closest Distance r = 10.0 km
Site dimension (z) = 100 m × 100 m
Map Accuracy = Approximately Located

## Slide 16: Sensitivity Case 1: Change source to SFZ
z = 100 m
r = 600 m
SFZ
0.60 km
Tests:
  Alternative Framing of Hazard Source
M 5.8
(L = 5.4 km)
Source Logic Tree
Suizenji
Fault Source
Magnitude
Mean Rate (×10-5 yr-1)
5.4
5
60
Max Rupture Length
Max Rupture Thickness
Average Dip
5.8
Mag PDF
Maximum
Magnitude
23.3
Notes:
Maximum magnitude PDF modeled as delta function (single magnitude at stated rate)
The rate is based on 4300 yr mean RI calculated using estimated 0.1 mm/yr slip rate and scaling using HERP methodology

## Slide 17: Sensitivity Cases – Kumamoto Site
Case 1: source is SFZ (not FFZ)
Site coordinates (x1,y1) – off-fault = 130.7417°, 32.7899°
Site dimension (z) = 100 m × 100 m
Closest Distance, FFZ: r = 0.60 km
Map Accuracy = Inferred
Case 2: site is ON FFZ (principal faulting)
Site coordinates (x2,y2) – on-fault = 130.7656°, 32.7474°
Distance r = 0 km
Also test Floating EQs
Case 3: site is ON SFZ (principal faulting)
Site coordinate (x3,y3) – on-SFZ = 130.7467°, 32.7936°
Closest Distance r = 0 km
Case 4: site is 10 km from FFZ
Site coordinate (x4,y4) – off-FFZ = 130.7196°, 32.8288°
Closest Distance r = 10.0 km
Site dimension (z) = 100 m × 100 m
Map Accuracy = Approximately Located

## Slide 18: Sensitivity Cases 2 and 3: Move site onto fault (r = 0); test floating
Tests:
  Magnitude and l/L variability
  How “floating” is treated
3
M 7.2
(46+32
= 78 km)
M 6.9
(24 + 22
= 46 km)
2
M 6.5
(22 km)
1
2
+
1
2
+
+
M 6.5
(floating)
M 5.8
(5.4 km)
FFZ, HERP sources
FFZ, branch alt
SFZ, additional
l/L =
0.23
l/L =
0.37
l/L =
0.37
l/L
varies
l/L =
0.39
2
3
+
M 7.0
(22 + 32
= 54 km)
l/L =
0.1

## Slide 19: Sensitivity Case 2: Source Logic Tree
Futagawa + Uto (1+2)
Fault Source
Magnitude
Mean Rate (×10-5 yr-1)
Max Rupture Length
Max Rupture Thickness
Average Dip
6.9
7.0
Mag PDF
46
14
68.6
Maximum
Magnitude
54
14
60
Maximum
Magnitude
l/L
0.37
Floating M 6.5 (1+2+3)
14
64.6
6.5
Maximum
Magnitude
64.2
variable
[0.5]
[0.5]
22
Uto (2)
1.28
3.53
Futagawa + Uto +
Uto-Hanto-North (1+2+3)
1.28
7.2
78
14
64.6
Maximum
Magnitude
0.37
Uto + Uto-Hanto-North (2+3)
0.10
~20
6.5
Maximum
Magnitude
18.9
0.23
14
60

## Slide 20: Sensitivity Cases – Kumamoto Site
Case 1: source is SFZ (not FFZ)
Site coordinates (x1,y1) – off-fault = 130.7417°, 32.7899°
Site dimension (z) = 100 m × 100 m
Closest Distance, FFZ: r = 0.60 km
Map Accuracy = Inferred
Case 2: site is ON FFZ (principal faulting)
Site coordinates (x2,y2) – on-fault = 130.7656°, 32.7474°
Distance r = 0 km
Also test Floating EQs
Case 3: site is ON SFZ (principal faulting)
Site coordinate (x3,y3) – on-SFZ = 130.7467°, 32.7936°
Closest Distance r = 0 km
Case 4: site is 10 km from FFZ
Site coordinate (x4,y4) – off-FFZ = 130.7196°, 32.8288°
Closest Distance r = 10.0 km
Site dimension (z) = 100 m × 100 m
Map Accuracy = Approximately Located

## Slide 21: Sensitivity Case 4: Site farther from principal fault (r > 0)
Tests:
  Magnitude and “r” variability
3
2
1
2
+
1
2
+
+
FFZ, r = 5.2 km
5.2 km
5.2 km
5.2 km
2
1
2
+
FFZ, r = 10 km
10 km
10 km
10 km
3
1
2
+
+
2
3
+
5.2 km
2
3
+
10 km

## Slide 22: Requested Results
PowerPoint or similar presentation format
Overview of fault displacement model per publication
Definition of the Intensity Measure
  e.g., Net fault displacement? Strike-slip or vertical displacement component?
  Localized on a single fault within the site? Cumulative offset across the site?
Fault displacement model logic tree for hazard calculation
Presentation of base case results (hazard curves)
Presentation of mean and fractile hazard curves (for base case with epistemic uncertainty)
Presentation of results for sensitivity cases

## Slide 23: Requested Results continued
Tabulated results: Hazard for the following displacement amplitudes (cm):
  0.01, 0.1, 0.5, 1, 1.5, 3, 5, 7.5, 10, 15, 30, 50, 75, 100, 300, 500, 750, 1000
Graphical results: Hazard curves showing annual exceedance frequency vs displacement (cm)
Base Case Hazard Curves, single source path
  Four “marginal” hazard curves and total mean hazard curve
Base Case Hazard Curves, epistemic uncertainty in source
  Total Mean Hazard Curve
  Hazard Fractile Curves: 5, 16, 50, 84, 95 percentiles
  Separate fractiles from source characterization versus fault displacement models (optional)
  “Tornado” or other sensitivity plots to examine contribution of parameter uncertainty to total hazard uncertainty (optional)

## Slide 24: Requested Results continued
Sensitivity #1
  Compare SFZ hazard curve versus Base Case mean hazard curve
Sensitivity #2
  Four “marginal” hazard curves and Total Mean hazard curve, r=0
  Hazard Fractile Curves: 5, 16, 50, 84, 95 percentiles
  Break out fractiles from source characterization versus fault displacement models (optional)
  Compare Uto (2) source marginal hazard curve for fixed location versus “floating” characterization
Sensitivity #3
  Compare SFZ hazard curve versus Base Case mean hazard curve for r=0
Sensitivity #4
  Four “marginal” hazard curves and Total Mean hazard curve, r=10 km

## Slide 25: Next Steps: Preparation for Step 2
Procedures for validation and testing results from other groups
  How many cases? Which cases? What is tolerance for “validation”?
Scope of Benchmarking in Step 2:
  Fault displacement model testing:
    Only validate/test as-published median models? E.g., through a set of clear assumptions.
    Test/explore different approaches to problem solving and logic-tree development? E.g., provide limited assumptions and allow/encourage more creativity
  Source characterization testing:
    Is this beyond scope? E.g., IAEA provides all parameters?
    Limited scope? IAEA provides all source logic tree values and weights, but groups show sensitivities? This is a code validation exercize?
    Within scope? Provide limited assumptions and allow/encourage alternative approaches to solving magnitude-recurrence relationship
  Hazard code / post-processing testing? Validate/compare methods for:
    Locating earthquake ruptures on a model fault plane (floating)
    Computing “r” and “l/L” distances
    Calculating the magnitude-recurrence relationship
    Calculating hazard fractiles

## Slide 26: For any questions and clarification please send an email to A.Valentini@iaea.org
Notes: Thank you!